Contractor Bid Form

For Collier County Owner Occupied Rehabilitation Program

Company Submitting Bid:

Homeowner Name:			Gonzalo & Maria Blanco

Address: 1381 19th Street SW				City & Zip Code:   Naples, FL 34117

Phone #: 	239-353-4589	 	 	Project #:		15-049R

| Description | Estimated Cost |
| --- | --- |
| Replace roof on house. Remove existing roof, underlayment, and damaged sheathing and properly dispose of all roofing debris. Replace underlayment and any damaged sheathing. Repair all fascia and soffits Replace all flashing. Install new shingle roof system over the underlayment. Use architectural grade, 30-year fiberglass asphalt shingles in accordance with Florida Building Code. Minimum 30-year warranty for shingles. Provide quote per sheet of plywood (or attach price sheet for wood) replacement) – to be replaced as needed | $____________ $____________ |
| Electrical/Plumbing Provide GFCI outlets as needed to meet current requirements. Evaluate existing main breaker (125 amp) and upgrade to 150 amp if needed to meet current code and use requirements. Ensure electrical panel is labeled properly. Install smoke detectors in all bedrooms. Correct wiring for water heater. Add discharge pipe to the pressure relief valve on water heater. | $____________ |
| Exterior Replace 5 screen panels on lanai. Repair or replace screen door for lanai. | $____________ |
| HVAC/Insulation Replace one section of AC duct work that has a tear. Evaluate and correct blockage or loose fitting that causes water to accumulate in AC catch pan. Replace attic insulation in three identified spots. | $____________ |
| Cabinets Replace water-damaged corner cabinet to match existing cabinets. | $____________ |
| TOTAL | $____________ |

Work to be performed in a workmanlike manner, in accordance with the Standard Rehabilitation Specifications, local codes and manufacturer’s specifications.  The contractor shall be responsible for repairs and/or reinstallations of materials/equipment/fixtures damaged or removed due to any error or omission.  Contractors shall properly dispose of all fixtures, materials and other items removed from the dwelling unless otherwise specified herein.  There must be a quoted price for each line item in the space provided or the bid will be ineligible for consideration.

Company Name

Company Representative’s

Name (printed)

Representative’s Signature

Mailing Address

Representative’s Phone Number

Email Address

Date Submitted					  Date Accepted

By my signature, I certify that ____________________ has verified license, liability insurance and proof of worker’s compensation as required by our contract.

Steven Kirk, President						Date

# Text boxes

The work bid form defines the scope of work at this residence to be performed as defined by the COLLIER COUNTY, FLORIDA CONSTRUCTION & REHAB STANDARDS.  Contractors are responsible for securing and paying for any permits required by the County to perform the work outlined in the scope below.  Bids shall be submitted as soon as possible to Dottie Cook at 750 South Fifth Street, Immokalee, FL 34142 or at dottiecook@ruralneighborhoods.org.

I hereby certify that I am a licensed contractor and am eligible to participate in the Collier County Owner Occupied Rehabilitation Program.  I will provide copies of my company’s license, liability insurance, and proof of worker’s compensation.  As necessary, I will purchase, install, replace and/or repair and deliver ALL items referenced within this bid document.