Contractor Bid Form

For Collier County Owner Occupied Rehabilitation Program

Company Submitting Bid:

Homeowner Name:			Franco & Adelita Garcia

Address: 2248 55th Street SW		City & Zip Code:   Naples, FL 34116

Phone #: 	239-692-2061		 	 Project #:		16-039R

| Description | Estimated Cost |
| --- | --- |
| Electrical Repair receptacle for water treatment system. Provide electrical source for fountain pump to eliminate extension cord. Label individual electrical circuits in main service panel. Evaluate and replace if needed two breakers in panel box that are from a different manufacturer. Repair receptacle in family room that hangs from junction box. Replace smoke detector outside guest bedrooms. Replace receptacles at lanai kitchen with GFCI receptacles. | $____________ |
| Plumbing Correct slow-draining showers in guest and master bathrooms. Shower in guest bath was once a tub and may be pitched incorrectly. Correct low pressure at master bath sink when both hot and cold water are used. Install sink stopper in guest bathroom. Provide air gap for dishwasher drain line to prevent contamination. Repair or replace stuck water valve to dishwasher. Evidence of copper pipe repairs appears in living room. Evaluate plumbing to determine if other repairs are needed. Install discharge pipe from the relief valve on the water heater. | $____________ |
| Water System Repair or replace water treatment system. | $____________ |
| Exterior Repairs Repair flashing at dryer vent and make roofing repairs as needed. Repair or replace wood door and frame at exterior door. | $____________ |
| HVAC Replace air filter. Clean ducts. | $____________ |
| Interior Repairs Repair floor in living room by filling it flush with the cement floor. Adjust strike plate on east guest bedroom door so door latches. Add strike plate to west guest bedroom door. Add door stop at guest bathroom. Clean dryer vent. | $____________ |
| Cabinets. Replace cabinets in guest and master bathrooms. Replace kitchen cabinet door and drawer that is damaged. | $____________ |
| Screen Enclosure Repair lanai cage and screening as needed. | $____________ |
| TOTAL | $____________ |

Work to be performed in a workmanlike manner, in accordance with the Standard Rehabilitation Specifications, local codes and manufacturer’s specifications.  The contractor shall be responsible for repairs and/or reinstallations of materials/equipment/fixtures damaged or removed due to any error or omission.  Contractors shall properly dispose of all fixtures, materials and other items removed from the dwelling unless otherwise specified herein.

Company Name

Company Representative (printed)

Representative’s Signature

Mailing Address

Representative’s Phone Number

Email Address

Date Submitted					  Date Accepted

By my signature, I certify that ____________________ has verified license, liability insurance and proof of worker’s compensation as required by our contract.

Steven Kirk, President						Date

# Text boxes

The work bid form defines the scope of work at this residence to be performed as defined by the COLLIER COUNTY, FLORIDA CONSTRUCTION & REHAB STANDARDS.  Contractors are responsible for securing and paying for any permits required by the County to perform the work outlined in the scope below.  Bids shall be submitted as soon as possible to Dottie Cook at 750 South Fifth Street, Immokalee, FL 34142 or at dottiecook@ruralneighborhoods.org.

I hereby certify that I am a licensed contractor and am eligible to participate in the Collier County Owner Occupied Rehabilitation Program.  I will provide copies of my company’s license, liability insurance, and proof of worker’s compensation.  As necessary, I will purchase, install, replace and/or repair and deliver ALL items referenced within this bid document.